Modules and progress
Trainer_top	Refactor
Activation_stack	Done
Dual port BRAM	Done
Backpropagator	Refactor
Weight controller	Implemented in backpropagator
Weight loader	Done
Weight updater	Done
Tiled tensor product	Done
Tiled vector adder	Done
Error controller	Implemented in backpropagator
Error fetcher	Done
Vector dot	Done
Activation LUT	Done
Vector subtract	Done
Error propagator	Done, could use more testing
Matrix vector multiplication	Done
Vector dot	Done
Matrix transpose	Done

---
Module name	Can overflow:
Trainer_top
Activation_stack
Dual port BRAM
Backpropagator
Weight controller
Weight loader
Weight updater
Tiled tensor product	Yes, parametrized out width, has error signal output
Vector add	Yes, parametrized out width, has error signal output
Error controller
Error fetcher	Contained modules overflow
Vector dot	Yes, parametrized out width, has error signal output
Activation LUT
Vector subtract	Yes, parametrized out width, has error signal output
Error propagator	Contained modules overflow
Matrix vector multiplication	Contained modules overflow
Vector MAC	Yes, parametrized out width, has error signal output
Vector dot	Yes, parametrized out width, has error signal output
Matrix transpose

---
Module name	Uses valid/ready protocol
Trainer_top
Activation_stack
Dual port BRAM
Backpropagator
Weight controller	yes
Weight loader	no need
Weight updater	yes
Tiled tensor product	yes
Vector add	yes
Error fetcher	yes
Vector dot	yes
Activation LUT	yes
Vector subtract	yes
Error propagator	yes
Matrix vector multiplication	yes
Vector dot	yes

---
Fixed point issues
How do we settle the issue of growing fixed point numbers? Every multiplication, the width of a fixed point is the summed width of the inputs, and every subtraction/addition, the width is the incremented width of the larger input.
Since the data is moving in a circle (previous delta reused to calculate the new delta, and weights constantly being updated), we need a large enough size for all of it without sacrificing precision. By picking a large enough value for the signal width, we can truncate signals without too much worry.
When multiplying two fixed point numbers, the fraction grows along with the integer part. We can solve the fraction part by truncating it to a predefined amount, and we can avoid issues with integer part by assigning enough width to it for it to not grow out of hand.
With a global FRACTION parameter setting the number of bits used for the fraction part, and WIDTH-FRACTION used for the integer part, we only need to specify the WIDTH parameter for each fixed point signal.
a_WIDTH
a
result
result_WIDTH == a_WIDTH+b_WIDTH-FRACTION
b_WIDTH
b

---
Option 1
a
1	0	1	1	0	0	0	1	0	1
* b
0	1	0	0	1	0	1	1	0	0
Truncated
Truncated
Kept
=
0	0	1	1	0	0	1	1	1	1	1	0	1	1	0	1	1	1	0	0
Result width not parametrized: the size of integer and fraction is kept.
The size of the result is the same as that of inputs.
integer
fraction
integer
fraction
integer
fraction

---
Option 2 - Adopted
a
1	0	1	1	0	0	0	1	0	1
* b
0	1	0	0	1	0	1	1	0	0
Truncated
Kept
=
0	0	1	1	0	0	1	1	1	1	1	0	1	1	0	1	1	1	0	0
Integer width parametrized: the fraction is truncated to match input, but the size of integer part can be larger than that of inputs.
For some input with size INTEGER_WIDTH + FRACTION, the size of the result is RESULT_INTEGER_WIDTH + FRACTION
integer
fraction
integer
fraction
INTEGER_WIDTH
fraction

---
Neural network nomenclature
L
L-1
L-2
L-3

---
Forward pass
Layer
weights
start
Layer controller
final output
start input
valid
layer
layer output
valid
inputs
layer
output
start
valid
active

---
Layer controller
We want to tap into this signal to receive activations for different layers
start
Input
aggregator
Output
aggregator
start input
OA_output
layer
layer input
final output
layer output
active
layer start

---
Layer & neurons
Neuron
Neuron
Neuron
Neuron
Layer
weights for layer
inputs
weights
outputs
inputs
weights
outputs
inputs
weights
outputs
inputs
weights
outputs

---
Top module
Top module
First layer inputs
Inputs
Forward
propagation
Stack
Layer l output
Layer l
Layer l output
Layer l-1 output
Sample #
Weights
W
Sample #
Sample #
Weight updates
Target
outputs
Backpropagator
Current
layer
Outputs
Layer l

---
Top module
Top module
First layer inputs
Inputs
Forward
propagation
Stack
Layer l output
Layer l
Layer l output
Layer l-1 output
Sample #
Weights
W
Sample #
Sample #
Weight updates
Target
outputs
Backpropagator
Current
layer
Outputs
Layer l

---
Ideally: Top module
Top module
First layer inputs
Inputs
Forward
propagation
Stack
Layer l output
Layer l
Layer l output
Layer l-1 output
Sample #
Weights
W
Sample #
Sample #
Weight updates
Target
outputs
Backpropagator
Current
layer
Outputs
Layer l

---
Forward module
Input
aggregator
Output
aggregator

---
Top module
Layer != MAX_LAYER ?
Layer ++
Layer != 0 ?
Layer --
Layer == MAX_LAYER
Forward
pass
Backward
pass
Layer == 0

---
Trainer top
Trainer_top
The trainer top module receives activations from the forward propagation module, and returns adjusted weight matrices.
The activations are saved in the stack and fed to the backpropagator module which holds the weights.
Z_stack
Activation
stack
Backpropagator
zn
zx
zx-1
wx
n
x

---
Trainer top
Trainer_top
The trainer top module receives activations from the forward propagation module, and returns adjusted weight matrices.
The activations are saved in the stack and fed to the backpropagator module which holds the weights.
Z_stack
Activation
stack
Backpropagator
zn
zx
zx-1
wx
n
x
Current
layer
Training
sample

---
Activation stack
Activation stack is a parametrizable model for storing NN activations with one data and address input, and two outputs.
The data is received from the forward propagation module, and is read by the backpropagation module.
The two read buses read consecutive layer activations starting from the output layer down.
Activation stack
Synchronous
Dual Port
BRAM
zx
zn
output_data0
input_data
zx-1
n
input_addr
output_data1
-1
x
input_wr_en
output_addr
NEURON_NUM parameter is the number of cells of input_data and output_data.
ACTIVATION_WIDTH is the width of each of the NEURON_NUM activations.
STACK_ADDR_WIDTH is the size of the addresses sent to the stack.

---
Backpropagator
Backpropagator
Weight
controller
δx
wx
zx-1
Error
controller
zx

---
Backpropagator
Backpropagator
Weight controller
zx-1
wx
δx
zx
Error
fetcher
Error
propagator
layer
δx-1
sample
prop_delta
Error controller
fetcher_delta

---
Backpropagator
Backpropagator
Weight controller
zx-1
wx
δx
Denotes a split – the FIFO protocol needs to be careful and wait for both ready signals
zx
Error
fetcher
Error
propagator
layer
δx-1
sample
prop_delta
Error controller
fetcher_delta

---
Backpropagator
Backpropagator
Weight controller
zx-1
wx
δx
zx
Error
propagator
layer
δx-1
Error
fetcher
sample
prop_delta
Error controller
fetcher_delta

---
Backpropagator
Backpropagator
Weight controller
zx-1
wx
δx
zx
Error
fetcher
Error
propagator
layer
δx-1
sample
prop_delta
Error controller
fetcher_delta

---
Weight controller
Weight controller
IDLE
Weight updater
zx-1
ax-1
start
Δwx
Tensor
product
wx+Δwx
σ
SIGMA
δx
LR
+
activation
stable
Weights
BRAM
UPDATE
x
wx
wx
rd_addr
FS
FS
update
finished
wr_addr
wr_data
Weight loader
Weight initialization

---
Weight controller
Weight controller
While the weights should be available always, we add a FIFO protocol to be able to distinguish whether we have worked on a new weight matrix, or the old one.
Weights bram only accepts a new input after it sent out an output
Weight updater
zx-1
ax-1
Δwx
Tensor
product
wx+Δwx
σ
δx
LR
+
Weights
BRAM
x
wx
wx
Fifo
splitter
rd_addr
wr_addr
wr_data
Weight loader
Weight initialization

---
Weight updater
Weight updater
Weight updater receives the neuron activations and their errors, and computes ΔW as a matrix product of a and δ. The updates matrix is added with the weights matrix and is sent out.
The product is calculated as a matrix product of a vertical vector a and a horizontal vector δ.
aL
Tensor
product
ΔwL
wL+ΔwL
δx
+
wL
MULT.
1
start
IDLE
0
product_finish
ADD.
2
adder_finish

---
Tiled tensor product
start
Tensor product is a generalized module that calculates the product of a vertical vector a and a horizontal vector b, as seen in the picture. On start, the result vector is cleared, and can be used once valid is high.
The number of multipliers and cycles can be controlled with the TILING_H and TILING_V parameters, which control the number of rows being processed in parallel and the number of elements processed per row at a time. The number of multipliers inferred can be then calculated as TILING_H*TILING_V.
Vector a is the vertical one, and b is the horizontal one, so the TILING_V affects a and TILING_H affect b.
counter_v
b
tile_b=b[counter_h:counter_h+TILING_H]
reset
result
tensor
product
Result
buffer
valid
a
tile_a∗tile_b
tile_a=a[counter_h:counter_h+TILING_H]
counter_h
Tiled tensor product
*The tiled tensor product is meant to be as application agnostic as possible, so it is not tied to the NN concepts.

---
Tiled tensor product logic
1		2		3
4		5		6
counter_h = 0;
counter_v = 0;
finish = 0;
Process tile
counter_h*TILING_H
>= width?
Tiling progress of a 5x5 table, tiled
with TILING_H=2 and TILING_V=3
n
counter_h++;
y
counter_v*TILING_V
>= height?
counter_v++;
counter_h=0;
finish = 0;

---
Tiled vector add
Tiled vector add
Tiled vector add sums two vectors a and b. The TILING parameter controls how many adders are created, affecting the number of cycles needed to add the two vectors.
The size of the vectors is determined by A_CELL_WIDTH and B_CELL_WIDTH parameters. The fractions are A_
+
result
Result buffer
+
finish
Finish
logic
+
a
b
+1
+1
counter
+1
+1
*This document might be too descriptive? Abstract the tiling logic away?
TILING
TILING

---
Error propagator
wL
zL-1
The error propagator passes errors through layers, going from top to bottom.
After the matrix and dot product, the width of the signal grows. How do we set the width of the signal without significantly raising the number of parameters?
By setting the width high enough and
σ
δL
δL-1
Matrix
vector
mult.
Dot
product
Error propagator

---
Error propagator
wL
zL-1
MATRIX_WIDTH*
MATRIX_HEIGHT
MATRIX_WIDTH
The error propagator passes errors through layers, going from top to bottom.
Since the input and output delta have the same cell width, we choose to prune to the same size after each module. The output from the matrix vector multiplication and the dot product have the size of delta.
σ
δL
δL-1
VECTOR_WIDTH ==
MATRIX_HEIGHT
MATRIX_WIDTH
Matrix
vector
mult.
Dot
product
Error propagator

---
Error propagator
wL
zL-1
T
σ’
δL
δL-1
a
a
a
Matrix
vector
mult.
Dot
product
Error propagator

---
Matrix vector multiplication
MVM
Vector MAC
Result
buffer
Vector MAC
result
vector
valid
Vector MAC
T
matrix
valid
logic
Counter
The matrix vector multiplication module receives a vector and a matrix and computes their product. The MVM creates a TILING_ROW vector MAC units that dot multiply and sum two vectors, and feeds them the vector and rows of the matrix. Result buffer stores the outputs of MACs in the appropriate addresses. The TILING_COL parameter controls the number of multipliers in the vector MAC modules. The total number of multipliers is TILING_COL*TILING_ROW.
TILING_ROW

---
Matrix vector multiplication
Matrix
=
Vector
*
Result vector
<=>
By transposing the matrix, we can perform the matrix vector multiplication by using a vector dot product on the matrix rows. The pink blocks in the image show an example.
.
=
Vector
Result vector
Matrix
transpose

---
Vector MAC
Tiled vector add
*
Result
buffer
+
result
*
*
a
b
valid
logic
valid
+1
+1
counter
Vector MAC unit computes the sum of a dot product of two vectors.
The TILING parameter controls the number of multipliers in the module
TILING

---
Vector MAC
Tiled vector add
*
Result
buffer
+
result
*
*
a
b
valid
logic
valid
+1
+1
counter
The summing of TILING products is done serially – one vector at a time.
Ideally an adder tree should sum the tile instead of a chain of adders.
TILING

---
Transpose module
Transpose
Magic
matrix
transpose
Transpose module takes a WIDTH*HEIGHT matrix of ELEMENT_WIDTH wide cells, and outputs a HEIGHT*WIDTH transposed matrix. The module is completely combinatorial.
Perhaps we should clock this module?

---
Backpropagator
Backpropagator
Weight controller
zx-1
wx
δx
Denotes a split – the FIFO protocol needs to be careful and wait for both ready signals
zx
Error
fetcher
Error
propagator
layer
δx-1
sample
prop_delta
Error controller
fetcher_delta

---
Backpropagator - revised
Backpropagator
We don’t need the last layer’s delta, so it should be disregarded. We add the picker module to choose between the deltas from the fetcher and propagator, and disregard the last layer delta.
Weight controller
zx-1
wx
δx
zx
Error
fetcher
Error
propagator
δx-1
sample
layer
prop_delta
Error controller
fetcher_delta

---
Error fetcher
valid
Error fetcher
Valid
logic
state
δ_valid
Error fetcher calculates the errors of the output layer, and chooses which error to push depending on the layer currently processed.
The z signal is the activation of the highest layer from which the error is calculated using the target stored in BRAM.
The delta signal is the error calculated from the previous layer, which is valid only when the layer processed is not the output layer.
The mux chooses between the delta signal and the calculated layer depending on whether the layer input is equal to the max layer.
The valid signal is high when delta from the input is valid and picked, or when the dot finishes processing the output activations.
layer
layer==L
δn
δ
0
1
zL
σ
σ’
sample
aL
sigma_der_z
Target
BRAM
y
δL
-
dot

---
Error fetcher - widths
dw – delta width
zw – neuron output width
sw – sample address width
aw – activation width
lw – layer index width
Error fetcher
zw
FS
σ
σ’
sw
aw
aw
Target
BRAM
aw
-
dot
dw
aw+1

---
LUT
LUT
x[counter]
lut[x1]
Dual port
LUT
x_buffer
result
x
lut[x2]
x[counter+1]
Valid
logic
valid
Counter
start
LUT converts an input vector into a vector of values from the ROM. On start, the counter is reset and the input vector is sampled two values at a time, which are ran through a dual port ROM and stored in a buffer. Once the counter value is equal to the vector size, the valid signal is raised.

---
LUT
LUT
x[counter]
lut[x1]
Dual port
LUT
x_buffer
result
x
lut[x2]
x[counter+1]
Valid
logic
valid
Counter
start
IDLE
RUN
start
counter>=NUM_NEURON

---
Error fetcher
Layer==L
start==1
sigma_valid
sigma’_valid
Subtracts the targets and activations, nothing passes through, valid signal is 0.
Waits until the layer input is equal to max layer. Passes delta and valid from input.
LUT
IDLE
SUBT
Subtraction
finished
Layer!=L
FINISH
DOT
Dot finished
Calculates the dot product from the output of the subtractor and sigma derivative. Nothing passes through, valid signal is 0.
Retains the calculated output as long as layer is the max layer. Valid is 1. When the layer changes, goes to IDLE.